## Slide 1: Application-Managed Flash
Sungjin Lee, Ming Liu, Sangwoo Jun, Shuotao Xu, Jihong Kim† and Arvind
Massachusetts Institute of Technology
†Seoul National University
14th USENIX Conference on File and Storage Technologies
February 22-25, 2016

## Slide 2: NAND Flash and FTL
NAND flash SSDs have become the preferred storage devices in consumer electronics and datacenters
FTL plays an important role in flash management
  The principal virtue of FTL is providing interoperability with the existing block I/O abstraction
NAND Flash
Databases
File-systems
KV Store
Flash Device
Host System
…
Block I/O Layer
Overwriting restriction
Limited P/E
cycles
Bad blocks
Asymmetric I/O operation
Flash Translation Layer (FTL)

## Slide 3: FTL is a Complex Piece of Software
Requires significant hardware resources (e.g., 4 CPUs / 1-4 GB DRAM)
Incurs extra I/Os for flash management (e.g., GC)
Badly affects the behaviors of host applications
FTL runs complicated firmware algorithms to avoid in-place updates and manage unreliable NAND substrates
Flash Translation Layer (FTL)
NAND Flash
Databases
File-systems
KV Store
Address
Remapping
Garbage Collection
I/O
Scheduling
Wear-leveling &
Bad-block
Flash Device
Host System
…
…
Block I/O Layer

## Slide 4: ..But, Its Functionality is Mostly Useless
Databases
File-systems
KV Store
…
Many host applications manage underlying storage in a log-like manner, mostly avoiding in-place updates
NAND Flash
Log-structured Host Applications
Block I/O Layer
Flash Device
Host System
Object-to-storage
Remapping
Versioning & Cleaning
I/O Scheduling
…
Flash Translation Layer (FTL)
Address
Remapping
Garbage Collection
I/O
Scheduling
Wear-leveling &
Bad-block
…
This duplicate management not only (1) incurs serious performance penalties but also (2) wastes hardware resources
Address
Remapping
Garbage Collection
I/O
Scheduling
Wear-leveling &
Bad-block
…
Flash Translation Layer (FTL)
Duplicate Management

## Slide 5: Which Applications???
F2FS
WAFL
Btrfs
NILFS
RethinkDB
LevelDB
RocksDB
FlexVol
BlueSky
LogBase
Hyder
SpriteLFS
BigTable
MongoDB
Cassandra
HDFS
Which Applications
???
LSM-Tree
File Systems
Key-value Stores
Databases
Storage Virtualization

## Slide 6: Question:
What if we removed FTL from storage devices and allowed host applications to directly manage NAND flash?

## Slide 7: Application-Managed Flash (AMF)
Host Applications (Log-structured)
Block I/O Layer
Flash Device
Host System
Object-to-storage
Remapping
Versioning & Cleaning
I/O Scheduling
…
NAND Flash
Flash Translation Layer (FTL)
Address
Remapping
Garbage Collection
I/O
Scheduling
Wear-leveling &
Bad-block
…
…
NAND Flash
Light-weight Flash Translation Layer
(2) The host runs almost all of the complicated algorithms
- Reuse existing algorithms to manage storage devices
(1) The device runs essential device management algorithms
- Manages unreliable NAND flash and hides internal storage architectures
AMF Block I/O Layer (AMF I/O)
(3) A new AMF block I/O abstraction enables us to separate the roles of the host and the device
Log-structured Host Applications
Object-to-storage
Remapping
Versioning & Cleaning
I/O Scheduling
…
…

## Slide 8: AMF Block I/O Abstraction (AMF I/O)
AMF I/O is similar to a conventional block I/O interface
  A linear array of fixed-size sectors (e.g., 4 KB) with existing I/O primitives (e.g., READ and WRITE)
Host Applications
A logical layout exposed to applications
Sector (4KB)
READ and WRITE
AMF Block I/O Layer
Host System
Flash Device
…
Minimize changes in existing host applications

## Slide 9: Append-only Segment
Segment: a group of 4 KB sectors (e.g., several MB)
  A unit of free-space allocation and free-space reclamation
Append-only: overwrite of data is prohibited
Host Applications
Host System
AMF Block I/O Layer
Flash Device
…
Segment (MB)
Appending new data (WRITE)
Overwrite
TRIM
Appending
Only sequential writes with no in-place updates
→ Minimize the functionality of the FTL

## Slide 10: Case Study with AMF
F2FS
WAFL
Btrfs
NILFS
RethinkDB
LevelDB
RocksDB
FlexVol
BlueSky
LogBase
Hyder
SpriteLFS
BigTable
MongoDB
Cassandra
HDFS
LSM-Tree
File Systems
Key-value Stores
Databases
Storage Virtualization
Which Applications
???

## Slide 11: Case Study with File System
Host Applications (Log-structured)
AMF Block I/O Layer
Object-to-storage
Remapping
Versioning & Cleaning
I/O Scheduling
…
…
NAND Flash
AMF Log-structured File System (ALFS)
(based on F2FS)
Host System
Flash Device
AMF Flash Translation Layer (AFTL)
Segment-level Address
Remapping
Wear-leveling &
Bad-block

## Slide 12: AMF Log-structured File System (ALFS)
Chart: 
| # of code lines
F2FS | 14987
ALFS | 16323
<A comparison of source-code lines of F2FS and ALFS>
ALFS is based on the F2FS file system
How did we modify F2FS for ALFS?
  Eliminate in-place updates
    F2FS overwrites check-points and inode-map blocks
  Change the TRIM policy
    TRIM is issued to individual sectors
How many new codes were added?
1300 lines

## Slide 13: How Conventional LFS (F2FS) Works
LFS
PFTL
Check-Point
Segment
Inode-Map
Segment
Data
Segment 0
Data
Segment 1
Data
Segment 2
Segment
Block with 2 pages
* PFTL: page-level FTL

## Slide 14: How Conventional LFS (F2FS) Works
LFS
CP
Check-Point
Segment
Inode-Map
Segment
CP
Data
Segment 0
Data
Segment 1
Data
Segment 2
IM
#0
A
B
C
D
E
B
F
G
CP
IM
#0
B
Invalid
Check-point and inode-map blocks are overwritten
CP
PFTL
* PFTL: page-level FTL

## Slide 15: How Conventional LFS (F2FS) Works
LFS
CP
Check-Point
Segment
Inode-Map
Segment
CP
Data
Segment 0
Data
Segment 1
Data
Segment 2
IM
#0
A
B
C
D
E
B
F
G
CP
IM
#0
B
IM
#0
A
B
C
D
E
F
G
B
CP
CP
CP
IM
#0
The FTL appends incoming data to NAND flash
PFTL
* PFTL: page-level FTL

## Slide 16: How Conventional LFS (F2FS) Works
LFS
CP
Check-Point
Segment
Inode-Map
Segment
CP
Data
Segment 0
Data
Segment 1
Data
Segment 2
IM
#0
A
B
C
D
E
B
F
G
CP
IM
#0
B
IM
#0
A
B
C
D
E
F
G
B
CP
CP
CP
IM
#0
A
C
D
E
The FTL triggers garbage collection
A
C
D
E
: 4 page copies and 4 block erasures
PFTL
* PFTL: page-level FTL

## Slide 17: How Conventional LFS (F2FS) Works
LFS
CP
Check-Point
Segment
Inode-Map
Segment
CP
Data
Segment 0
Data
Segment 1
Data
Segment 2
IM
#0
A
B
C
D
E
B
F
G
CP
IM
#0
B
IM
#0
A
B
C
D
E
F
G
B
CP
CP
CP
IM
#0
A
C
D
E
A
C
D
E
The LFS triggers garbage collection
A
C
D
A
C
D
A
C
D
D
A
C
TRIM
: 3 page copies
PFTL
* PFTL: page-level FTL

## Slide 18: How ALFS Works
ALFS
AFTL
Check-Point
Segment
Inode-Map
Segment
Data
Segment 0
Data
Segment 1
Data
Segment 2
Segment
Segment with 2 flash blocks

## Slide 19: How ALFS Works
ALFS
AFTL
Check-Point
Segment
Inode-Map
Segment
Data
Segment 0
Data
Segment 1
Data
Segment 2
A
B
C
D
E
B
F
G
CP
IM
#0
CP
IM
#0
B
CP
CP
IM
#0
CP
CP
A
B
C
D
IM
#0
CP
E
B
F
G
IM
#0
CP
No in-place updates
No obsolete pages – GC is not necessary

## Slide 20: How ALFS Works
ALFS
AFTL
Check-Point
Segment
Inode-Map
Segment
CP
IM
#0
CP
IM
#0
CP
CP
IM
#0
CP
CP
A
B
C
D
IM
#0
CP
E
B
F
G
IM
#0
CP
Data
Segment 0
Data
Segment 1
Data
Segment 2
A
B
C
D
E
B
F
G
B
A
C
D
A
C
D
A
B
C
D
TRIM
A
C
D
The ALFS triggers garbage collection
: 3 page copies and 2 block erasures

## Slide 21: Comparison of F2FS and AMF
F2FS |  | AMF
File System | PFTL | File System
3 page copies | 4 copies + 4 erasures | 3 copies + 2 erasures
7 copies + 4 erasures |  | 3 copies + 2 erasures
Duplicate Management

## Slide 22: Experimental Setup
Implemented ALFS and AFTL in the Linux kernel 3.13
Compared AMF with different file-systems
  Two file-systems: EXT4 and F2FS with page-level FTL (PFTL)
Ran all of them in our in-house SSD platform
  BlueDBM developed by MIT

## Slide 23: Performance with FIO
For random writes, AMF shows better throughput
F2FS is badly affected by the duplicate management problem

## Slide 24: Performance with Databases
AMF outperforms EXT4 with more advanced GC policies
F2FS shows the worst performance

## Slide 25: Erasure Counts
AMF achieves 6% and 37% better lifetimes than EXT4 and F2FS, respectively, on average

## Slide 26: Resource (DRAM & CPU)
FTL mapping table size
Host CPU usage
SSD Capacity | Block-level FTL | Hybrid FTL | Page-level FTL | AMF
512 GB | 4 MB | 96 MB | 512 MB | 4 MB
1 TB | 8 MB | 186 MB | 1 GB | 8 MB

## Slide 27: Conclusion
We proposed the Application-Managed Flash (AMF) architecture.
  AMF was based on a new block I/O interface, called AMF IO, which exposed flash storage as append-only segments
  Based on AMF IO, we implemented a new FTL scheme (AFTL) and a new file system (ALFS) in the Linux kernel and evaluated them using our in-house SSD prototype
  Our results showed that DRAM in the flash controller was reduced by 128X and performance was improved by 80%
Future Work
  We are doing case studies with key-value stores, database systems, and storage virtualization platforms

## Slide 28: Source Code
All of the software/hardware is being developed under the GPL license
Please refer to our Git repositories
  Hardware Platform: https://github.com/sangwoojun/bluedbm.git
  FTL: https://github.com/chamdoo/bdbm_drv.git
  File-System: https://bitbucket.org/chamdoo/risa-f2fs
Thank you!